## Slide 1: Redfish Extensions for FPGAs
DMTF Redfish Forum
September 2018

## Slide 2: Disclaimer
The information in this presentation represents a snapshot of work in progress within the DMTF.
This information is subject to change without notice. The standard specifications remain the normative reference for all information.
For additional information, see the Distributed Management Task Force (DMTF) website.

## Slide 3: Redfish Extensions Summary
 | Use Case | Modeling Requirements | Redfish Model Changes
FPGA Resource | Client can determine the FPGAs that are in the system | Model FPGA characteristics | Add properties to Processor resource
FPGA Support Functions | Client can determine the functions supported by the FPGA | Model the acceleration functions on an FPGA | Add AccelerationFunction singleton and AccelerationFunctionCollection collection resource
FPGA Metrics | Client can obtain the FPGA metrics | Model the metrics available from an FPGA | Add ProcessorMetrics as a subordinate resource

## Slide 4: FPGA Functional Diagram
An FPGA can execute one or more code images call Acceleration Functions
Acceleration Functions may be loaded into the FPGA, at any time (including runtime)
The FPGA is visible to the host software as PCIe functions
  The FPGA is presented as the physical function
  The acceleration functions are accessible as virtual functions
FPGA
CPU
FPGA FW
Reconfiguration Slot
Reconfiguration Slot
BMC
Acceleration Function
Code
Acceleration Function
Code
Host
Interface
Sideband
Interface
External Interface
External Interface
External Interface
External Interface
PCIe PF
PCIe VF
PCIe VF
External interfaces are connected off-platform (e.g. Ethernet interfaces).
Reconfiguration slots are entities created by the FPGA FW used to program the Acceleration Function Code

## Slide 5: FPGA Redfish Model
The ProcessorType enum already contains "FPGA"
The reference between Endpoint and Acceleration Functions uses the “Processor” type
Service Root
CS_1
Fabric2
Edpt1
Zone1
FPGA_1
AC_1
Endpoints
Zones
Acceleration
Functions
Processors
Systems
Fabrics
FPGA
FPGA FW
Reconfiguration Slot
Reconfiguration Slot
Acceleration Function
Code
Acceleration Function
Code
PCIe PF
PCIe VF
PCIe VF
Processor Metrics
Chassis1
Chassis

## Slide 6: Model FPGA Characteristics & Accelerator Functions
{
"@odata.id": "/redfish/v1/Systems/CS_1/Processors/FPGA_1",
"Id": "FPGA1",
"Socket": "CPU 1",
"ProcessorType": "FPGA",
"ProcessorArchitecture": "OEM",
"InstructionSet": "OEM",
"Manufacturer": "Intel(R) Corporation",
"Model": "Aria10",
"UUID": "00000000-0000-0000-0000-000000000000",
"MaxTDPWatt": 150,
"IntegratedMemory": [
{
"MemoryType": "HBM2",
"CapacityMiB": 512,
"SpeedMHz": 1066
}
],
"FPGA": {},
"Metrics": {},
"AccelerationFunctions": {}
"Links": {
"Endpoints": [],
"ConnectedProcessors": [],
"PCIeDevice": {},
"PCIeFunctions": []
}
}
{
"FpgaType": "Discrete",
"Model": "Aria10",
"FirmwareId": "0x6400002fc614bb9",
"FirmwareManufacturer": "Intel (R) Corporation",
"FirmwareVersion": "Blue v.1.00.86",
"HostInterface": {
"InterfaceType": "PCIe",
"PCIe": { "MaxPCIeType": "Gen4", "MaxLanes": 8 }
},
"ExternalInterfaces": [
{
"InterfaceType": "Ethernet",
"Ethernet": { "MaxSpeedMbps": 10240, "MaxLanes": 4 }
}
],
"PCIeVirtualFunctions": 1,
"ProgrammableFromHost": true,
"ReconfigurationSlots": [
{
"SlotId": "AFU0",
"UUID": "00000000-0000-0000-0000-000000000000",
"ProgrammableFromHost": true,
"AccelerationFunctionLink": {
"@odata.id": "/redfish/v1/Systems/1/Processors/FPGA1/Functions/Compression"
}
}
]
}
In Processor resource: add FPGA object, add subordinate Metric resource, and add reference links

## Slide 7: Model FPGA Metrics
{
"@odata.context": "/redfish/v1/$metadata#ProcessorMetrics.ProcessorMetrics",
"@odata.id": "/redfish/v1/Systems/1/Processors/CPU1/Metrics",
"@odata.type": "#ProcessorMetrics.v1_0_0.ProcessorMetrics",
"Id": "Metrics",
"Name": "Processor Metrics",
"Description": "Processor Metrics",
"Status": {
"State": "Enabled",
"Health": "OK",
"HealthRollup": null
},
"Cache": [],
"BandwidthPercent": 62,
"AverageFrequencyMHz": 2400,
"ThrottlingCelsius": 65,
"TemperatureCelsius": 41,
"ConsumedPowerWatt": 82,
"FrequencyRatio": 0.00432,
"LocalMemoryBandwidthBytes": 18253611008,
"RemoteMemoryBandwidthBytes": 81788928,
"KernelPercent": 2.3,
"UserPercent": 34.7,
"CoreMetrics": []
}
"CoreMetrics": [
{
"CoreId": "core0",
"InstructionsPerCycle": 1.16,
"CstateResidency": [
{ "Level": "C0", "Residency": 1.13 },
{ "Level": "C1", "Residency": 26 },
{ "Level": "C3", "Residency": 0.00878 },
{ "Level": "C6", "Residency": 0.361 },
{ "Level": "C7", "Residency": 72.5 }
]
}
]
"Cache": [
{
"Level": 3,
"CacheMiss": 0.12,
"CacheHitRatio": 0.719,
"CacheMpi": 0.00088,
"OccupancyBytes": 3030144,
"OccupancyPercent": 90.1
}
]

## Slide 8: Proposal – Schema Changes
CSDL File | Description
Processor_v1.xml | Resource updated to show FPGA characteristics
AccelerationFunctionCollection_v1.xml | New collection resource
AccelerationFunction_v1.xml | New singleton resource
ProcessorMetrics_v1.xml | New resource